## Slide 1: Comparison of various trajectory-tracking controllers using UR5 robot
-ADITYA GUPTE , GOKUL NARAYANAN, JOSHUA RAJ, SINAN MORCEL

## Slide 2: Introduction: Motivation
Generating Trajectories for manipulators – easy
Tracking trajectories effectively – hard (but also depends)
  Unknown Dynamics
  Approximate Dynamics
  Gravity Compensation
  Friction and Actuator Saturation (non-linear terms)
  Tuning gains
  Singularities

## Slide 3: Problem Statement
Comparing the performance of the following controllers
  Inverse Dynamic Controller
    Baseline for comparison
  Robust Feedback Linearization controller
    Robust to disturbance (parametric uncertainty)
  Passivity Based Controller
    Constant bound on the uncertainty
    Better Robustness Properties
  Reinforcement Learning based controller
    model free controller
Benchmark trajectory set
  Straight line trajectory
  Circular trajectory

## Slide 4: Pipeline
Matlab
ODE Simulation
Simulink
Animation
Matlab
Plots,Videos

## Slide 5: Methodology

## Slide 6: Disclaimers
Dynamic model may not be accurate
Considering only position control
Considering errors in the mass of the first 3 links only
Errors random in every iteration
Simulink is only an animation tool
There is loss of time information for the videos

## Slide 7: Challenges faced
Dealing with actual system dynamics is difficult.
Actual dynamics not provided but just a URDF
The dynamics you find online are approximations which may not work well with urdf given

## Slide 8: So what about the RL controller?
Reinforcement learning based controller. Working with robots rquires to work in continious domain , thus causing us to use function aprroximators.
Traditional Rl uses: tables as approximators
Other fuction approximators used : neural networks, radial basis functions,etc .
Continuous space is always haeder to work with and you should not underestimate the transition

## Slide 9: Controllers implemented
Inverse dynamics control in task space.
Passivity based control in task space
Robust feedback Linearization in task space
Passivity based robust control in task space

## Slide 10: Inverse Dynamics Controller in Task Space
Dynamic equation of the system:
Compute control input:
For this controller we need an accurate dynamic model

## Slide 11: Passivity Based Control in Task Space
Control Input:

## Slide 12: Robust feedback Linearization in task space
if
if
where,

## Slide 13: Passivity based robust control in task space
Control Input :
  Parameter Update:
    if
    if

## Slide 14: Passivity based robust control in task space
Where
Control input:
if
if
Here depends only on Inertia parameters. Hence the design

## Slide 15: Results – Circular trajectory
Perfect Dynamics
Imperfect Dynamics
Inverse Dynamic Controller

## Slide 16: Results
Perfect Dynamics
Imperfect Dynamics
Passivity Based Controller

## Slide 17: Results
Perfect Dynamics
Imperfect Dynamics
Robust Controller

## Slide 18: Results
Perfect Dynamics
Imperfect Dynamics
Passivity based Robust Controller

## Slide 19: Results – Straight Line trajectory
Perfect Dynamics
Imperfect Dynamics
Inverse Dynamics Controller

## Slide 20: Results
Perfect Dynamics
Imperfect Dynamics
Passivity Controller

## Slide 21: Results
Perfect Dynamics
Imperfect Dynamics
Robust Controller

## Slide 22: Results
Perfect Dynamics
Imperfect Dynamics
Passivity Based Robust Controller

## Slide 23: VIDEOS
Quetions?
Thank You!

## Slide 24: Discussion